## Slide 1: CSCE 5580 – Computer Networks Instructor: Tao Wang

## Slide 2: Tentative Topics
Computer Networks and the Internet
Application Layer
Transport Layer
Network Layer
Link Layer and Local Area Networks
Wireless and Mobile Networks
Multimedia Networking
Security in Computer Networks

## Slide 3: Aim of the Course
Introduce the concepts behind the design and implementation of:
  Computer Networks
  Communication Protocols
Provide you with analytical skills to design new protocols.
Welcome to the world of computer networks!!

## Slide 4: Some cool pics!

## Slide 5: History of Internet
http://www.youtube.com/watch?v=9hIQjrMHTv4

## Slide 6: Chapter 1: introduction
Chapter goal:
Get “feel,” “big picture,” introduction to terminology
  more depth, detail later in course
Overview/roadmap:
What is the Internet? What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Protocol layers, service models
Security
History

## Slide 7: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization
Notes: Switches and routers are connected to devices, their job is to transfer packages from router to router.
Communication links can be wired or wireless.
Network: The right-side image is a network consisting of sub-networks.

## Slide 8: “Fun” Internet-connected devices
Web-enabled toaster +
weather forecaster
Internet phones
Slingbox: remote
control cable TV
Security Camera
IP picture frame
Internet
refrigerator
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress
Amazon Echo
Others?
Gaming devices
cars
scooters
bikes
Pacemaker & Monitor
AR devices
Fitbit
diapers

## Slide 9: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4/5G, Ethernet
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force
Notes: Internet standards can sometimes define protocols.

## Slide 10: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events
Notes: Protocols define rules for the way to send messages.

## Slide 11: What’s a protocol?
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET https://computerscience.engineering.unt.edu

## Slide 12: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 13: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Notes: Edge (host): Mobile phones, Laptops, Desktops, etc.

## Slide 14: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links

## Slide 15: A closer look at Internet structure
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
  interconnected routers
  network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Notes: The routers use only the Network layer and the link layer.

## Slide 16: Links: physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps Ethernet
Notes: Ethernet cable is nothing but twisted pairs.
It connects the desktop to the router.

## Slide 17: Links: physical media
Coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple frequency channels on cable
  100’s Mbps per channel
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (10’s-100’s Gbps)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise
Notes: Coaxial cable connects the Modem and service providers.
It can support high speed.
Fiber cable can provide higher speed.

## Slide 18: Links: physical media
Wireless radio
signal carried in various “bands” in electromagnetic spectrum
no physical “wire”
broadcast, “half-duplex” (sender to receiver)
propagation environment effects:
  reflection
  obstruction by objects
  Interference/noise
Radio link types:
Wireless LAN (WiFi)
  10-100’s Mbps; 10’s of meters
wide-area (e.g., 4G/5G cellular)
  10’s Mbps (4G) over ~10 Km
Bluetooth: cable replacement
  short distances, limited rates
terrestrial microwave
  point-to-point; 45 Mbps channels
satellite
  up to < 100 Mbps (Starlink) downlink
  270 msec end-end delay (geostationary)
Notes: All radio link types have different speeds, coverages, etc.
Bluetooth: Used for low-power and short-distance transmission.

## Slide 19: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models

## Slide 20: The network core
mesh of interconnected routers
The fundamental question: how is data transferred through the network?
  Circuit-switching: continuous and dedicated
  Packet-switching: chunks of data and discrete
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Notes: 2 methods to transmit the data.
Circuit-switching:
  Continuous means data streams not as packages.
  Reserve all the resources for the sender and receiver.
Packet-switching:
  Divide data into packets and send them to the destination.
  Discrete means the resources is not reserved.
  Packet-switching is more populate now-a-days in the internet.

## Slide 21: Circuit switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks
Notes: Red line resources are reserved.

## Slide 22: Circuit switching: FDM and TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
Time Division Multiplexing (TDM)
time divided into slots
each call allocated its own band, can transmit at max rate of that narrow band
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band (only) during its time slot(s)
Notes: 2 ways to allocate resources in circuit switching.
Both diagram supports 4 users at the same time.
Divide the channel based on frequency and time.

## Slide 23: Packet switching
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
Resource contention:
Backlog: aggregate resource demand can exceed amount available
Congestion: packets queue, wait for link use
Store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Notes: Resources are not divided.
Too many devices connected to the router – That’s why the ping is high while playing the game.

## Slide 24: Packet switching
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Sequence of A & B packets does not have fixed pattern, bandwidth shared on demand  statistical multiplexing.
Notes: Routes have local storage.
All the packages are stored in the queue.
If the local storage is full – packet loss may happen.

## Slide 25: Packet switching: store-and-forward
packet transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
Q: Why we use stop-and-forward?
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec
Notes: This is also used in today's internet.
The router will wait until it gets the complete packets. After it gets the full package then it sends to the destination.
Push packet to link is transmission delay.
After the packet is in link, it can travel in speed of light.
For packet switching it requires the entire packet.
If we send the 1st half and then 2nd half, the 2nd half will not have headed, so it cannot identify which part of packet it is.

## Slide 26: Packet switching versus circuit switching
example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
Q: how many users can use this network under circuit-switching and packet switching?
N
users
1 Gbps link
…..
circuit-switching: 10 users
Q: how did we get value 0.0004?
packet switching: with 35 users, probability > 10 active at same time is less than .0004 *

## Slide 27: Packet switching versus circuit switching
great for “bursty” data – sometimes has data to send, but at other times not
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior with packet-switching?
  “It’s complicated.” We’ll study various techniques that try to make packet switching as “circuit-like” as possible.
Is packet switching a “slam dunk winner”?